## Slide 1: Introduction to Networked Graphics
Part 5 of 5: Application Support & Recent Research

## Slide 2: Overview
Goal:
  To explain some other application issues and areas of recent research.
Topics:
  Security and secure networks
  Streaming
  Cluster graphics
  Thin clients
  Peer to peer

## Slide 3: Overview of Security Problems
ServerX
ClientB
ClientA
ClientC
ClientC may be interfering with traffic
ClientA may be running
Compromised code
ClientB may be colluding
with ClientA
ServerX may have
exploitable bugs
Notes: Figure 13.1

## Slide 4: Compromised Clients
A pervasive problem in gaming
  E.G. notable problems with PSNet games after the PS3 master key was found allowing modified code on the PS3
For console gaming, hardware vendors try to lock down the hardware so only verified programs can run
For PC gaming, various detection techniques such as PunkBuster that detect malicious software
  Countermeasure are typically ahead of amateur cheats but not professional cheats

## Slide 5: Traffic Interference
Once data is on the network it is public
Various attacks
  Packet injection
  Packet hiding
  Latency asymmetry
Some are mitigated by secure networks
  Some servers specifically support secure protocols for certain actions
Notes: For Packet Injection see the discussion between John Carmack and Richard Stalman regards the opening and exploitation of the Quake source code and protocol. O

## Slide 6: Exploitable Server
Users need to trust server
  User-hosted games are not accepted for ranking tournaments or cash games
Server might be have a loophole
  E.G. Dupe bugs
Denial of service attack
  E.G. Deny a win to an opponent by crashing the score server

## Slide 7: User Collusion
A very difficult social situation to counter
  E.G. Chip dumping
With this and all other security problems monitoring of exceptions is important
  Players being too skillful
  Unlikely plays
  Game inventory inflation

## Slide 8: Virtual Private Networks
Now very common for corporations and universities
Three reasons
  Protection of internal services
  Giving a different “appearance” to the outside world (e.g. ACM Digital Library)
  Security of access from anywhere (no need to trust local network)
The very easiest way to protect a NVE or NG is to require someone go on a trusted VPN first
  Incurs latency/bandwidth overhead of routing all information to the VPN access point first

## Slide 9: Virtual Private Networks (VPNs)
ClientA
ServerX
ServerY
IP
IP
Notes: ClientA can’t contact ServerY directly. Probably a firewall prevents access.

## Slide 10: VPNs and IPSec
ClientA
ServerX
ServerY
VPN
Gateway
IPSec
IP
IP
Notes: ClientA connects to a VPN using IPSec (IP Secure). All traffic between them is encrypted. ClientA can now reach ServerY, but additionally to any other server, it looks as if they are on the LAN that includes ServerY.

## Slide 11: Different Uses of Streaming
Streaming Protocols
Streaming Animations
Streaming Geometry (i.e. incremental download)

## Slide 12: Streaming Protocols
Audio/video transport is well developed on the Internet
However “well developed” means lots of competing solutions
Several plug and play libraries
Real-Time Protocol an extension of UDP to support streaming (though not all streaming protocols use it)
Can get RTP compliant libraries which enables streaming and receiving
  E.G. AccessGrid, some VoIP solutions

## Slide 13: Real-Time Protocol
Bits | 0 15 |  | 16 31
0-31 | Version, config, flags | Payload Type | Sequence Number
32-63 | Timestamp |  | 
64-95 | Synchronisation Source (SSRC) Identifier |  | 
96+ | Contributing Source (CSRC) Identifiers (Optional) |  | 
96+ | Header Extensions (Optional) |  | 
96+ | Payload Header |  | 
128+ | Payload Data |  | 
Notes: Figure 13.4

## Slide 14: RTP Payloads
Notes: Table 13.1

## Slide 15: Streaming Animations
We have already looked at streaming positions and orientations of objects
However, a large class of objects are humans or animals (or aliens) which deform
Typically modeled from the graphics side as a skeleton
Animation is controlled by indicating which motion the character is in and the keyframe in that motion
Because motion is continuous (e.g. motion capture) information might only need to be sent > 1s

## Slide 16: Examples of Keyframe Animation
Notes: Figure 13.5

## Slide 17: Streaming Geometry
Many NVEs use very large worlds which need to be downloaded because user modifiable or just vast
System needs to determine which parts of the models should be transferred
Typically done in a priority order from the viewpoint of the client, e.g. in increasing distance order
Two ways of doing this
  Client-pull
  Server-push

## Slide 18: Server Push
Client
Server
PositionX
Send AHigh, BLow
Send BHigh, CLow
PositionY
Position Z
Send DLow, ELow

## Slide 19: Client Pull
Client
Server
Fetch Index
Send Index
Send BHigh, CLow
Fetch AHigh, BLow
Send AHigh, BLow
Fetch BHigh, CLow

## Slide 20: Clusters
Cluster graphics is a particular concern of Virtual Reality system designers
One GPU card generates one or two video to get maximum throughput, but we might need 4+ displays
Need to synchronize graphics at two levels
  Synchronize graphics state on input to rendering
  Need to synchronize video output

## Slide 21: Layers of Sharing Graphics
Application
Scene Graph
Graphics Drivers
Modifies scene graph
Render traversal
Application
Scene Graph
Graphics Drivers
Copy scene graph
Synchronize applications
Copy render commands
Notes: Figure 13.9

## Slide 22: Tools
Copy render commands
  E.G. Chromium – stream OpenGL commands over TCP/Ethernet, or other non-IP-based interconnects
Copy scene graph
  E.G. OpenSG – stream an edit change list for a scene-graph
Synchronize applications
  E.G. VRJuggler – isolate all input in to one (or more) C++ classes that can serialize themselves to the network, stream the resulting serializations.

## Slide 23: Thin Clients
Might be considered “backwards” but graphics architectures go in circles, so why not networked graphics architectures
Render the graphics on a server, stream the results as video
Recent consumer examples: OnLive, OToy, GaiKai
However many OS vendors have such a functionality for supporting thin clients over LANs

## Slide 24: Thin Clients
Very small installable on client, client doesn’t need to be high-powered (hence thin client, e.g. tablet)
Stream your controller input to server
Stream back video (e.g. 720p from OnLive) OR stream back window rendering code (X11, RDP, OpenGL derivatives)

## Slide 25: Thin Clients: Pros & Cons
Main pro: install cost close to zero, immediate start
Main con(1): latency
  No question that some actions (e.g. camera rotation) are very easily noticeable
BUT consider OnLive: the server can run both game client and game server
  Multiuser might be fairer (to be investigated!)
  Almost like playout delay via video!
  (N.B. OnLive actual architecture not revealed)
Main con(2): bandwidth required

## Slide 26: Peer to Peer
A live challenge: how can peer to peer networks scale up to very large numbers
Key to this is how to distribute awareness management
A secondary issue is how to “bootstrap”: how does a user find their local users?

## Slide 27: Larger Peer to Peer Context
Enormous work in networking community on generic large scale peer to peer databases
Key technologies
  Distributed hash tables: a way of storing data sets across multiple hosts but ensuring fast (O(log(N))) access to any data item
  Application-level routing: a mechanism for supporting group peer to peer communication without any underlying network support

## Slide 28: Within a NVE Context
Very active line of research
For example, can one maintain a set of closest peers with something similar to a Voronoi Tessellation?
If peers can identify their Voronoi Cell, they can identify their neighbours.
New clients can walk the cells to get to find their true neighbours

## Slide 29: Summary
Plenty of tools and options to support your NG or NVE project
Security is a big challenge if you can’t get your users on to a VPN
Other facilities require more infrastructure and are very domain specific
Plenty of research issues: thin clients being a wild card at the moment